DOSING SHEET

GRANMATTINO

| Author: | Approved: |  |
| --- | --- | --- |
| Eprom Date: 12/10/99 | Version: Rev.1.2I | Country: Italy |
| Code: F957100 | Model: C4/1 |  |

## SELF-SERVICE VERSION

| DOSE CODE | WATER | INGREDIENT |
| --- | --- | --- |
|  | dec. | cc. | d.s. | gr. |
| CA1 Espresso coffee (bean) | 82 | 40 | 0 | 0 |
| CA2 Double Espresso coffee (bean) | 102 | 55 | 0 | 0 |
| CA3 Long coffee (bean) | 112 | 60 | 0 | 0 |
| CA4 Coffee for white espresso (bean) | 82 | 40 | 0 | 0 |
| CA5 Coffee for cappuccino (bean) | 82 | 40 | 0 | 0 |
| LA1 White for white espresso | 16 | 25 | 10 | 2 |
| LA2 White for cappuccino | 35 | 55 | 19 | 4 |
| LA3 White for cappu with choc | 25 | 40 | 19 | 4 |
| LA4 White for creamichoc | 19 | 30 | 15 | 3 |
| KA1 Coffee for cappu with choc (bean) | 82 | 40 | 0 | 0 |
| KA2 Choc for cappu with choc | 14 | 25 | 6 | 3.5 |
| KA3 White for tea | 0 | 0 | 0 | 0 |
| KK1 Chocolate | 50 | 90 | 33 | 21 |
| KK2 Strong chocolate | 50 | 90 | 42 | 24 |
| KK3 Choc for creamichoc | 33 | 60 | 25 | 16 |
| TE1 Tea black | 0 | 0 | 0 | 0 |
| TE2 Tea for white tea | 0 | 0 | 0 | 0 |
| DE1 Instant coffee (normal) | 23 | 40 | 20 | 1.2 |
| DE2 Instant coffee (large) | 32 | 55 | 20 | 1.2 |
| BR1 Soup | 0 | 0 | 0 | 0 |
| AC1 Hot water | 33 | 100 | 0 | 0 |
| PC1 ½ Jug of coffee (bean) | 706 | 400 | 0 | 0 |
| PL1 ½ Jug of whitener | 250 | 400 | 185 | 40 |
| PK1 ½ Jug of chocolate | 160 | 400 | 145 | 80 |
| PT1 ½ Jug of instant coffee | 160 | 400 | 97 | 6 |
| PA1 ½ Jug of hot water | 167 | 500 | 0 | 0 |
| PD1 Not used | 0 | 0 | 0 | 0 |
| PC2 Jug of coffee (bean) | 1412 | 800 | 0 | 0 |
| PL2 Jug of whitener | 500 | 800 | 370 | 80 |
| PK2 Jug of chocolate | 325 | 800 | 290 | 160 |
| PT2 Jug of instant coffee | 325 | 800 | 193 | 12 |
| PA2 Jug of hot water | 340 | 1000 | 0 | 0 |
| PD2 Not used | 0 | 0 | 0 | 0 |

DOSING SHEET

GRANMATTINO

| Author: | Approved: |  |
| --- | --- | --- |
| Eprom Date: 12/10/99 | Version: Rev.1.2I | Country: Italy |
| Code: F957100 | Model: C4/1 |  |

SELF-SERVICE VERSION

| DEFAULT WATER VOLUMES BY SELECTION |
| --- |
| SELECTION | VOLUME |
| Espresso | 40cc |
| Double espresso | 55cc |
| Long coffee (bean) | 60cc |
| White coffee (bean) | 65cc |
| Cappuccino (bean) | 95cc |
| Cappuccino with chocolate (bean) | 105cc |
| Chocolate | 90cc |
| Strong chocolate | 90cc |
| Creamichoc | 90cc |
| Instant coffee | 40cc |
| Long instant coffee | 55cc |
| Hot water | 100cc |

N.B.  The volumes for the ½ and full jugs are shown in the dosing table.

DOSING SHEET

GRANMATTINO

| Author: | Approved: |  |
| --- | --- | --- |
| Eprom Date: 12/10/99 | Version: Rev.1.2I | Country: Italy |
| Code: F957100 | Model: C4/1 |  |

## HOTEL VERSION

| DOSE CODE | WATER | INGREDIENT |
| --- | --- | --- |
|  | dec. | cc. | d.s. | gr. |
| CA1 Espresso coffee (bean) | 82 | 40 | 0 | 0 |
| CA2 Double Espresso coffee (bean) | 102 | 55 | 0 | 0 |
| CA3 Long coffee (bean) | 112 | 60 | 0 | 0 |
| CA4 Not used | 0 | 0 | 0 | 0 |
| CA5 Coffee for cappuccino (bean) | 82 | 40 | 0 | 0 |
| LA1 Whitener | 69 | 110 | 42 | 9 |
| LA2 White for cappuccino | 35 | 55 | 19 | 4 |
| LA3 White for cappu with choc | 25 | 40 | 19 | 4 |
| LA4 White for creamichoc | 19 | 30 | 15 | 3 |
| KA1 Coffee for cappu with choc (bean) | 82 | 40 | 0 | 0 |
| KA2 Choc for cappu with choc | 14 | 25 | 6 | 3.5 |
| KA3 White for tea | 0 | 0 | 0 | 0 |
| KK1 Chocolate | 50 | 90 | 33 | 21 |
| KK2 Strong chocolate | 50 | 90 | 42 | 24 |
| KK3 Chocolate for creamichoc | 33 | 60 | 25 | 16 |
| TE1 Tea black | 0 | 0 | 0 | 0 |
| TE2 Tea for white tea | 0 | 0 | 0 | 0 |
| DE1 Instant coffee (normal) | 23 | 40 | 20 | 1.2 |
| DE2 Instant coffee (large) | 32 | 55 | 20 | 1.2 |
| BR1 Soup | 0 | 0 | 0 | 0 |
| AC1 Hot water | 33 | 100 | 0 | 0 |
| PC1 ½ Jug of coffee (bean) | 706 | 400 | 0 | 0 |
| PL1 ½ Jug of whitener | 250 | 400 | 185 | 40 |
| PK1 ½ Jug of chocolate | 160 | 400 | 145 | 80 |
| PT1 ½ Jug of instant coffee | 160 | 400 | 97 | 6 |
| PA1 ½ Jug of hot water | 167 | 500 | 0 | 0 |
| PD1 Not used | 0 | 0 | 0 | 0 |
| PC2 Jug of coffee (bean) | 1412 | 800 | 0 | 0 |
| PL2 Jug of whitener | 500 | 800 | 370 | 80 |
| PK2 Jug of chocolate | 325 | 800 | 290 | 160 |
| PT2 Jug of instant coffee | 325 | 800 | 193 | 12 |
| PA2 Jug of hot water | 340 | 1000 | 0 | 0 |
| PD2 Not used | 0 | 0 | 0 | 0 |

DOSING SHEET

GRANMATTINO

| Author: | Approved: |  |
| --- | --- | --- |
| Eprom Date: 12/10/99 | Version: Rev.1.2I | Country: Italy |
| Code: F957100 | Model: C4/1 |  |

HOTEL VERSION

| DEFAULT WATER VOLUMES BY SELECTION |
| --- |
| SELECTION | VOLUME |
| Espresso (bean) | 40cc |
| Double espresso (bean) | 55cc |
| Long coffee (bean) | 60cc |
| Whitener | 110cc |
| Cappuccino (bean) | 95cc |
| Cappuccino with chocolate (bean) | 105cc |
| Chocolate | 90cc |
| Strong chocolate | 90cc |
| Creamichoc | 90cc |
| Instant coffee | 40cc |
| Long instant coffee | 55cc |
| Hot water | 100cc |

N.B.  The volumes for the ½ and full jugs are shown in the dosing table.

DOSING SHEET

GRANMATTINO

| Author: | Approved: |  |
| --- | --- | --- |
| Eprom Date: 12/10/99 | Version: Rev.1.2I | Country: Italy |
| Code: F957100 | Model: C4/1 |  |

### INGREDIENT DELAY

The default ingredient delay is 0.6 seconds.

OTHER INFORMATION:

The software monitors the temperature of the whitener ingredient motor.

ALTERNATIVE SELECTIONS

#### BLACK TEA IN PLACE OF INSTANT COFFEE

#### Set the water and powder doses for instant coffee in DE1 & DE2 to 0

Set the water dose for tea in TE1 to 57 (100cc)

Set the powder dose for tea in TE1 to 4 (0.5g)

Set the water dose for tea white in TE2 to 37 (70cc)

Set the powder dose tea white in TE2 to 4 (0.5g)

Set the water dose for whitener for tea in KA3 to 19 (30cc)

Set the powder dose for whitener for tea in KA3 to 10 (2g)

SOUP IN PLACE OF INSTANT COFFEE

#### Set the water and powder doses for instant coffee in DE1 & DE2 to 0

Set the water dose for soup in BR1 to 96 (120cc)

Set the powder dose for soup in BR1 to 80 (10.5g)

Disable selection 8

DOSING SHEET

GRANMATTINO

| Author: | Approved: |  |
| --- | --- | --- |
| Eprom Date: 12/10/99 | Version: Rev.1.2I | Country: Italy |
| Code: F957100 | Model: C4/1 |  |

##### SELECTION COMPOSITION

| SELECTION | BASE | 1st ADDITION | 2nd ADDITION |
| --- | --- | --- | --- |
|  | Water | Powder 1 | Powder 2 | Water | Powder 1 | Powder 2 | Water | Powder |
| Espresso | CA1 | CA1 | - | - | - | - | - | - |
| Double espresso | CA2 | CA2 | - | - | - | - | - | - |
| Long coffee | CA3 | CA3 | - | - | - | - | - | - |
| White coffee ** | CA4 | CA4 | - | LA1 | LA1 | - | - | - |
| Cappuccino | CA5 | CA5 | - | LA2 | LA2 | - | - | - |
| Cappu with choc | KA1 | KA1 | - | LA3 | LA3 | - | KA2 | KA2 |
| Chocolate | KK1 | KK1 | - | - | - | - | - | - |
| Strong chocolate | KK2 | KK2 | - | - | - | - | - | - |
| Creamichoc | KK3 | KK3 | - | LA4 | LA4 | - | - | - |
| Instant coffee | DE1 | DE1 | - | - | - | - | - | - |
| Long in.coffee | DE2 | DE2 | - | - | - | - | - | - |
| Hot water | AC1 | AC1 | - | - | - | - | - | - |
| ½ jug coffee | PC1 | PC1 | - | - | - | - | - | - |
| ½ jug whitener | PL1 | PL1 | - | - | - | - | - | - |
| ½ jug chocolate | PK1 | PK1 | - | - | - | - | - | - |
| ½ jug in.coffee | PT1 | PT1 | - | - | - | - | - | - |
| ½ jug hot water | PA1 | PA1 | - | - | - | - | - | - |
| Jug coffee | PC2 | PC2 | - | - | - | - | - | - |
| Jug whitener | PL2 | PL2 | - | - | - | - | - | - |
| Jug chocolate | PK2 | PK2 | - | - | - | - | - | - |
| Jug in.coffee | PT2 | PT2 | - | - | - | - | - | - |
| Jug hot water | PA2 | PA2 | - | - | - | - | - | - |

** In the Hotel version white coffee is replaced by whitener and only uses LA1.

DOSING SHEET

GRANMATTINO

| Author: | Approved: |  |
| --- | --- | --- |
| Eprom Date: 12/10/99 | Version: Rev.1.2I | Country: Italy |
| Code: F957100 | Model: C4/1 |  |

##### CANISTER LAYOUT

MINI-DIP SETTINGS

| MACHINE VERSION | DIP 1 |
| --- | --- |
| HOTEL | OFF |
| SELF-SERVICE | ON |

| ELECTRICAL SUPPLY | DIP 2 |
| --- | --- |
| THREE PHASE | OFF |
| SINGLE PHASE | ON |

| MACHINE VERSION | DIP 3 | DIP 4 |
| --- | --- | --- |
| INSTANT WITH 5 CANISTERS | OFF | OFF |
| ESPRESSO | ON | OFF |
| INSTANT WITH 4 CANISTERS | ON | ON |

| PAYMENT SYSTEM | DIP 6 | DIP 7 | DIP 8 |
| --- | --- | --- | --- |
| NONE | OFF | OFF | OFF |
| VALIDATOR (single vend) | ON | OFF | OFF |
| VALIDATOR (multi-vend) | OFF | ON | OFF |

N.B. MINI-DIP 5 IS NOT USED AND SHOULD BE OFF.

# Text boxes

- BEANS

- WHITENER

- CHOCOLATE

- IN. COFFEE

### OR IN.TEA         OR SOUP